Remote Sensing Survey

of the Walla Walla River Basin

Thermal Infrared and Color Videography

Watershed Sciences, LLC

712 NW Fourth Street

Corvallis, OR 97330

FINAL REPORT

Prepared for the

Oregon Department of Environmental Quality

Portland OR 98124-3755

Revised: May 9, 2002

# Introduction

Forward Looking Infrared (FLIR) has been demonstrated as a reliable, cost-effective, and accessible technology for monitoring and evaluating stream temperatures from the scale of watersheds to individual habitats (Karalus et al., 1996; Norton et al., Faux et al., 1998).  In 2000, the Oregon Department of Environmental Quality (ODEQ) contracted with Watershed Sciences, LLC to map and assess stream temperatures in portions of the Walla Walla River Basin.

Traditional methods for monitoring stream temperatures have relied on in-stream temperature monitors.  These monitors provide temporally continuous data, but furnish no insight into the spatial variability in temperatures.  With the use of remote sensing, we have been able to map stream temperatures across entire stream networks for the time of the survey.  FLIR technology has proven to be a highly portable and cost-effective method to collect very detailed data over large areas in very little time.   The combination of temporally and spatially continuous data provides very powerful tools for understanding the dynamics of stream temperature hierarchically across multiple scales (pools ( reaches ( streams ( watersheds).  Current research has identified cool versus warm streams within a watershed, cool reaches within a stream, and cool habitats within a reach (McIntosh et al., 1995; Torgerson et al., 1995; Torgerson et al., 1999).

The results and analysis presented here are at the watershed and tributary scales.  This report provides longitudinal temperature profiles for each stream surveyed as well as a discussion of the thermal features observed in the basin.  FLIR and associated color video images are included in the report in order to illustrate significant thermal features.  An ArcView GIS database provided with this report includes all of the images collected during the survey and is structured to allow analysis at finer scales.

# Methods

## Data Collection

The ODEQ contracted with Watershed Sciences, LLC of Corvallis, Oregon to collect and analyze thermal infrared and visible video imagery for the Walla Walla River during the summer of 2000.  The survey was conducted on August 15, 2000 and covered the Walla Walla River and the South Fork Walla Walla River for a total of 67.7 river miles (Figure 1).  Data collection was timed to capture daily maximum stream temperatures, which typically occur between 14:00 and 18:00 hours.  Table 1 summarizes the date, time, and survey distance for each surveyed stream.

Data were collected using a FLIR and a Day TV video camera co-located in a gyro-stabilized mount that attached to the underside of a helicopter.   The helicopter was flown longitudinally over the center of the stream channel with the sensors in a vertical (or near vertical) position.   All streams were surveyed upstream and flight altitude was selected based on the estimated average stream channel width.   In general, the flight altitude was selected so that the stream channel occupied approximately 20% of the image frame.

Figure 1 – Map of the Walla Walla River Basin showing the extent of the FLIR and color video survey and for August 15, 2000.

Table 1 – Date, time, and distance for streams surveyed in the Walla Walla River Basin.

| Stream | Date | Local Time (PM) | Miles Surveyed |
| --- | --- | --- | --- |
| Walla Walla River | 15 August 00 | 14:07 – 15:48 | 50.6 |
| South Fork Walla Walla River | 15 August 00 | 15:49 – 16:20 | 17.1 |
| Total Miles Surveyed | 67.7 |

FLIR data were collected digitally and recorded directly from the sensor to an on-board computer.  The FLIR detects emitted radiation at wavelengths from 8-12 microns and records the level of emitted radiation in the form of an image.  Each image pixel contains a measured value that can be directly converted to a temperature.   The raw FLIR images represent the full 12 bit dynamic range of the instrument and were tagged with time and position data provided by a Global Positioning System (GPS).   Each thermal image frame covers a ground area of approximately 100 x 150 meters and has a spatial resolution of  < 0.5 meters/pixel.  For all other streams each thermal image covers a ground area of approximately 100 x 150 meters and has a spatial resolution of about 0.25 meters/pixel.

Day TV images were recorded to an on-board digital videocassette recorder at a rate of 30 frames/second.  GPS time and position were encoded on the recorded video.  The Day TV sensor was aligned to present the same ground area as the thermal infrared sensor.  The GPS time coding provides a means to correlate Day TV images with the FLIR images during post-processing.  The day TV video supplements the interpretation and analysis of the FLIR images.  In addition, day TV video provides a record of the conditions in the basin at the time of the survey.

## Data Processing

A computer program was used to scan the FLIR imagery and create an ArcView GIS point coverage containing the image name, time, and location it was acquired.  The coverage provided the basis for assessing the extent of the survey and for integrating it with other spatially explicit data layers in the GIS.  This allowed us to identify the images associated with the ground truth locations.  The data collection software was used to extract temperature values from these images at the location of the in-stream recorder.  The radiant temperatures were then compared to the kinetic temperatures from the in-stream data loggers.

The image points were associated with a river kilometer using the dynamic segmentation features of Arc/Info GIS software.  The river kilometers were derived from 1:100K “routed” stream covers from the Environmental Protection Agency  (EPA).  The route measures provide a spatial context for developing longitudinal temperature profiles of stream temperature.

In the laboratory, a computer algorithm was used to convert the raw thermal images (radiance values) to ARC/INFO GRIDS where each GRID cell contained a temperature value.  A GIS program was used to display the GRID associated with an image location selected in the point coverage. The GRID was color-coded to visually enhance temperature differences, enabling the user to extract temperature data.  The GRIDS were classified in one-degree increments over the temperature range of 5 to 30oC.  Temperatures < 5oC are black, temperatures between 30 and 50oC were colored in shades of gray (darker tones -> lighter tones), temperatures  > 50oC are white.

Figure 2 illustrates a color coded GRID displayed in the ArcView environment.  This GRID illustrates the confluence of the Walla Walla River and the Columbia River.  The legend on the left of the “Grid View” specifies the temperature range associated with each color.  The other view window shows the point coverage with the displayed GRID location highlighted in yellow.  Each blue point in the “Thermal Survey” view represents another image location.

Figure 2 – ArcView display showing a color-coded temperature GRID in one window and the geographic location of the GRID in the other. The orientation of the image is always in the flight direction.

Once in the GRID format, the images were analyzed to derive the minimum, maximum, and median stream temperatures.  To derive these measures, an ArcView program was used to sample the GRID cell (temperature) values in the stream channel.  Ten sample points were taken longitudinally in the center of the stream channel.  Samples were taken once every 3 to 4 images to provide complete coverage without sampling the same water twice (there is approximately 40-60% overlap between images).  Where there were multiple channels, only the main channel (as determined by width and continuity) was sampled.  In cases where the channel was obscured by vegetation, as was the situation on many of the tributaries, the next image where the stream channel was clearly visible was sampled.  For each sampled image, the sample minimum, maximum, median, and standard deviation was recorded directly to the point coverage attribute file.  The median value is the most useful measure of stream temperatures because it minimizes the effect of extreme values.  Figure 3 shows a pseudo-color thermal image and corresponding day TV image.  The red “x’s” on the image show typical sample locations.  Temperature sampling focuses on the center of the stream channel.

The temperature of tributaries and other detectable surface inflows were also sampled from images.  These inflows were sampled at their mouth using the same techniques described for sampling the main channel.  If possible, the surface inflows were identified on the USGS 24K base maps.  The inflow name and median temperature were then entered into the point coverage attribute file.

Day TV images corresponding to the FLIR images were extracted from the database using a computer-based frame grabber.  The images were captured to correspond to the thermal infrared images and provide a complete coverage of the stream.  The video images were “linked” to the corresponding thermal image frame in the ArcView GIS environment.

Figure 3 – Thermal/Day TV image pair showing typical temperature sampling locations

(red x’s).  These samples determine the median stream temperature for this image frame.

## Data Limitations

FLIR systems measure thermal infrared energy emitted at the water surface.  Since water is essentially opaque to thermal infrared wavelengths, the sensor is only measuring the surface water temperature.   This is typically not an issue on streams where the water column is thoroughly mixed.  Field measurements conducted on the Middle Fork of the John Day River, OR and on the Klamath River, CA confirmed that thermal stratification was insignificant or not present even in the deepest pools.  However, stratification has been observed behind impoundments and in deep slow moving channels.  We found no evidence of thermal stratification in the Walla Walla River Basin.

# Results

## Thermal Accuracy

Temperatures from in-stream data loggers were compared to radiant temperatures derived from the imagery for the Walla Walla River Basin (Table 2).  The radiant temperature derived from the imagery represents the average of 10 points sampled from the image at the data logger location.  The in-stream temperature at the date and time the image was acquired was then compared to the radiant temperature derived from the image.  If a consistent difference was

observed for all the in-stream sensors in given stream, the parameters used to convert radiant values to temperatures were adjusted to provide a better fit to the in-stream sensors.

Table 2 provides a comparison of the in-stream and radiant temperatures.  A total of 4 points were used to assess the temperature accuracy of the imagery.  Of the 4 locations, 3 showed a difference of less then (0.5oC (contract specifications) between the FLIR image and the in-stream data logger.  Overall the accuracy for the 4 points was (0.4oC, which is consistent with previous work.  The factors that influence the accuracy of the radiant temperature calculations are spatial.  Therefore, it is important to consider accuracy on a stream-by-stream basis.

Table 2.  Comparison of instream water temperatures with radiant temperatures derived from thermal infrared images for the Walla Walla River Basin streams, August 15, 2000.  Temperatures are reported in °C and river mile measures are cited for locations.

| Location | River mile | File ID | Image frame | Time PM | Stream Temp. (Ts) | Radiant Temp. (Tr) | Difference (Tr – Ts) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Walla Walla R. |  |  |  |  |  |  |  |
| Upstream of Route 12 bridge | 10.4 | 88442 | Wal0503 | 14:25 | 22.4 | 21.4 | -1.0 |
| Near church | 32.8 | 349773 | Wal1833 | 15:14 | 22.4 | 22.3 | -0.1 |
| Milton-Freewater | 46.2 | 68514 | Wal2539 | 15:41 | 17.8 | 17.9 | 0.1 |
| South Fork Walla Walla R. | 7.7 | 345269 | Wal3181 | 16:02 | 13.1 | 13.5 | 0.4 |

## Analysis of Thermal Imagery

The median temperatures for each sampled image of the Walla Walla River and South Fork Walla Walla River were plotted versus the corresponding river mile (Figure 4).  The plot also contains the median temperature of all surface water inflows (e.g., tributaries, canals) that were visible in the imagery where they input into the mainstem rivers.  Tributaries are labeled in Figure 4 by river mile with their name and temperature listed in Table 3.  Only the surface water inflows that could be positively identified in the imagery were included.  In some cases, tributaries and other surface water inputs were obscured by riparian vegetation or outside the sensor field of view and their image location could not be accurately determined.

At the upstream end of the survey (RM 67.7) the South Fork of the Walla Walla River was very cold (8.1 oC, Figure 5).  From RM 67.7 to the confluence with the Walla Walla River and the North Fork Walla Walla River (RM 50.6) stream temperatures in the South Fork increase slowly in the downstream direction, reaching the maximum (15.4oC) at the confluence with the Walla Walla River.  We detected three tributaries in this reach with two the same temperature as the South Fork and one being warmer (Figures 15-17).  At the confluence with the Walla Walla River, the North Fork Walla was contributing warmer flows (20.1oC, Figure 14).  From the confluence with the Forks downstream to RM 42.9, stream temperatures in the Walla Walla River increase rapidly, reaching the survey maximum (25.5oC), just downstream of Milton Freewater, Oregon.  In the area around Milton Freewater, streamflows decrease rapidly due to irrigation diversion, causing stream temperatures to increase rapidly.  From RM 42.9 to RM 42.0 the stream channel is either completely dry or isolated pools of water.   Below RM 42.0, streamflows become continuous again.  Flows are very low in this reach with stream temperatures increasing to a local maximum (24.1oC) at RM 38.6. At RM 38.3, Yellowhawk Creek contributes cooler flows (20.3oC, Figure 13), decreasing the Walla Walla to 20.9 oC.  Over the next 4 miles stream temperatures remain relatively constant with additional cooler flows from the East Fork Walla Walla River (19.0oC, RM 37.4, Figure 12).  From RM 34.5 to RM 28.6, stream temperatures increase steadily in the downstream direction, reaching a local maximum of 25.8oC.  From RM 28.6 to the confluence with the Columbia River, stream temperatures tended to decrease in the downstream direction, flowing into the Columbia at 19.3oC.  Over the 67.7 miles that were surveyed we detected 11 tributaries contributing flows to the Walla Walla and South Fork Walla Walla River.  Three of the tributaries were contributing cooler flows with the remaining eight contributing warmer flows (Table 3).

Figure 4.  Longitudinal temperature profile of the Walla Walla and South Fork Walla Walla Rivers (8/15/00).  Tributaries identified by river mile are listed in Table 3.

Figure 5.  Longitudinal temperature profile for the South Fork Walla Walla River (8/15/00).

Table 3 – Tributaries and other surface inflows identified during the FLIR survey of the Walla Walla and South Fork Walla Walla Rivers.  Tributaries correspond to those shown in Figure 4.

| Tributary | River Mile | Tributary Temp (*C) | Mainstream Temp (*C) | Difference |
| --- | --- | --- | --- | --- |
| Unnamed (LB) | 1.6 | 22.4 | 20.5 | 1.9 |
| Unnamed (RB) | 2.0 | 21.8 | 21.8 | 0.0 |
| Touchet River (RB) | 19.4 | 23.4 | 21.9 | 1.5 |
| Pine Creek (LB) | 21.8 | 23.1 | 22.8 | 0.3 |
| Dry Creek (RB) | 27.0 | 18.9 | 24.6 | -5.7 |
| Spring (LB) | 29.3 | 23.6 | 24.3 | -0.7 |
| Irrigation Diversion (LB) | 30.5 | 22.5 | 22.9 | -0.4 |
| Irrigation Diversion (LB) | 30.9 | 22.6 | 22.7 | -0.1 |
| Irrigation Canal (RB) | 31.4 | 22.6 | 22.4 | 0.2 |
| Mill Creek (RB) | 33.4 | 23.3 | 21.6 | 1.7 |
| East Little Walla Walla R. (LB) | 37.5 | 19.0 | 21.4 | -2.4 |
| Yellowhawk Creek (RB) | 38.4 | 20.0 | 23.2 | -3.2 |
| Spring (LB) | 41.1 | 16.4 | 19.8 | -3.4 |
| Spring (RB) | 41.1 | 16.9 | 20.6 | -3.7 |
| Spring (RB) | 42.5 | 16.0 | 16.1 | -0.1 |
| Canal (RB) | 43.0 | 21.9 | 25.5 | -3.6 |
| Spring (LB) | 43.7 | 15.2 | 21.6 | -6.4 |
| North Fork (RB) | 50.5 | 20.1 | 15.4 | 4.7 |
| Burnt Cabin Gulch (LB) | 64.7 | 12.1 | 10.0 | 2.1 |
| Spring (LB) | 65.9 | 7.0 | 9.3 | -2.3 |
| Skiphorton Creek (RB) | 67.6 | 6.5 | 8.7 | -2.2 |

#### Summary

# A FLIR survey of the Walla Walla and South Fork Walla Walla River was conducted on August 15, 2000 covering a survey distance of 67.7 miles.  Timing of the daily surveys was targeted at mid-afternoon to capture maximum daily stream temperatures.  Stream temperatures in the headwaters were very cold with temperatures decreasing in a downstream direction.  Irrigation withdrawals and dry channels in some reaches resulted in elevated stream temperatures in many reaches of the lower river, particularly around the town of Milton Freewater, Oregon.

Bibliography

Karalus, R.S., M.A. Flood, B.A. McIntosh, and N.J. Poage. 1996. ETI surface water

quality monitoring technologies demonstration. Final Report. Las Vegas, NV: Environmental Protection Agency.

McIntosh, B.A., R.N. Faux, and J.R. Sedell.  1999.  Aerial survey of the Applegate River:

thermal infrared and color videography.  Final Report.  Rogue River National Forest.  27 pp.

McIntosh, B.A., D. M. Price, C.E. Torgerson, and H.W. Li. 1995. Distribution,

habitat utilization, movement patterns, and the use of thermal refugia by spring chinook in the Grande Ronde, Imnaha, and John Day basins.  Progress Report. Portland, OR: Bonneville Power Administration, Project No. 93-700. 16 pp.

Norton, D.J., M.A. Flood, B.A. McIntosh [and 14 others]. 1996. Modeling, monitoring

and restoring water quality and habitat in Pacific Northwestern watersheds. Final Report. Washington D.C.: Environmental Program, Government Applications Task Force, Central Intelligence Agency, 68 pp.

Torgerson, C.E., D.M. Price, H.W. Li, and B.A. McIntosh. 1995. Thermal refugia and

chinook salmon habitat in Oregon: applications of airborne thermal videography.

In: Proceedings of the 15th Biennial Workshop on Color Photography and

Videography in Resource Assessment. Terre Haute, ID: American Society for

Photogrammetry and Remote Sensing. Pages 167-171.

Torgerson, C.E., D.M. Price, H.W. Li, and B.A. McIntosh. 1999. Multiscale thermal

refugia and stream habitat associates of chinook salmon in Northeastern Oregon. Ecological Applications. 9(1), pp 301 – 319.

Image Figures

Figure 6 - FLIR/Day TV image pair (frame: wall0058) showing the Walla Walla River (20.5oC) and an unnamed tributary (22.4oC) on the left bank at river mile 1.6.

Figure 7 - FLIR/Day TV image pair (frame: wall0234) showing a side-channel (22.6oC) along the left bank (looking downstream) at river mile 5.5 of the Walla Walla River (21.9oC).

Figure 8 - FLIR/Day TV image pair (frame: wall1000) showing the Touchet River (23.4oC) entering the Walla Walla River (21.9oC) on the right bank at river mile 19.4.

Figure 9 - FLIR/Day TV image pair (frame: wall1239) showing Pine Creek (23.1oC) entering the Walla Walla River (22.8oC) on the left bank at river mile 21.8.

Figure 10 - FLIR/Day TV image pair (frame: wall1527) showing Dry Creek (18.9oC) entering the Walla Walla River (24.6oC) on the right bank at river mile 27.0.

Figure 11 - FLIR/Day TV image pair (frame: wall1887) showing Mill Creek (23.3oC) entering the Walla Walla River (21.6 oC) on the right bank at river mile 33.4.

Figure 12 - FLIR/Day TV image pair (frame: wall2097) showing the East Little Walla Walla River (19.0oC) entering the Walla Walla River (21.4 oC) on the left bank at river mile 37.5.

Figure 13 - FLIR/Day TV image pair (frame: wall2148) showing Yellowhawk Creek (20.0oC) entering the Walla Walla River (23.2oC) on the right bank at river mile 38.4.

Figure 14 - FLIR/Day TV image pair (frame: wall2787) showing the North Fork Walla Walla River (20.1oC) entering the Walla Walla River (15.4oC) on the RB at river mile 50.6.

Figure 15 - FLIR/Day TV image pair (frame: wall3298) showing a side channel (12.9oC) entering the South Fork of the Walla Walla River (12.3oC) along the left bank at river mile 60.3.

Figure 16 - FLIR/Day TV image pair (frame: wall3546) showing Burnt Creek (12.1oC) entering the South Fork of the Walla Walla River (10.0oC) on the left bank at river mile 64.7.

Figure 17 - FLIR/Day TV image pair (frame: wall3573) showing and unnamed tributary entering the South Fork of the Walla Walla River (12.6oC) on the left bank at river mile 65.2.  Due to the small channel width and intervening vegetation, an accurate sample of the tributary’s temperature at its mouth could not be sampled.

Figure 18 - FLIR/Day TV image pair (frames: wall3615-3620) showing an apparent spring (7.0oC) along the left bank of the South Fork Walla Walla River (9.3oC) at river mile 65.9.

# Footnotes

Geographic Information System

# Text boxes

x

x

xX

x

x

x

x

x

x

x