Oregon Department of Fish and Wildlife

Threemile Creek Bull Trout Protection, #97-112-007

Final Report

Oregon Department of Fish and Wildlife on behalf of the Klamath Basin Bull Trout Working Group (Working Group), applied for a National Fish and Wildlife Foundation challenge grant to provide a three month seasonal for the Threemile Creek Bull Trout Protection Project.  ODFW was awarded the grant and conducted activities from June 23 to September 23 1997.  The primary objective of the project was to remove and suppress non-native fish species (brook trout and bull trout/brook trout hybrids) in upper Threemile Creek through the use of electrofishing, night snorkel spearing, and experimental trapping.  In addition, data on existing macroinvertebrate, mollusk and amphibian populations was to be collected in case chemical treatment becomes necessary for complete removal of exotic fish species in the future.  The project was completed through the cooperation of ODFW, Klamath Tribes and the Klamath Falls Soil and Water Conservation District.

Brook trout removal activities were conducted on Threemile Creek beginning in late June, and ending in late September 1997.  The 110 road culvert was the lower extent of the project area.  The culvert was chosen as the beginning point because it is a barrier to upstream fish movement, in particular brook trout.  Removal activities stopped at the uppermost bull trout distribution limit.  A total of 11 block nets (13mm bar mesh) were set, creating 11 reaches.  The block nets were placed to restrict fish movement, aid in brook trout/hybrid removal, and assist in coordinating field activities.  Removal efforts consisted of electrofishing in the brook trout zone and night snorkel spearing in the bull trout intergrade zone (both brook trout and bull trout present).  Electrofishing was conducted from the culvert to block net 6.  Night snorkel spearing was conducted from block net 6 to block net 11.  All block nets were removed by late September 1997.  The objective of both electrofishing and night snorkel spearing activities were to remove as many brook trout and bull trout/brook trout hybrids as possible.

Electrofishing

The end of the electrofishing zone (brook trout zone) was determined by electrofishing upstream of the 110-road culvert until two bull trout were encountered.  The location of the second bull trout determined the end of the electrofishing zone.  The second bull trout was located where block net 6 was placed.  Both bull trout encountered were removed above block net 6 where only snorkel removal activities would be conducted.  This allowed electrofishing to be conducted from the 110-road culvert to block net 6 without being concerned of possible injury to any bull trout.  Six reaches were established in the brook trout electrofishing zone.  Each reach was approximately .3 miles long.  From the culvert to block net 6, a total of 121 brook trout were removed.  For the 121 brook trout removed, 92 were greater than 90 mm in length.  One hybrid was removed from the culvert to block net 6.

Electrofishing Date for Threemile Creek activities, 1997.

|  |  | Reach | # Passes | All BKT | BKT > 90mm | Hybrid |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Culvert - BN 1 | 5 | 7 | 6 |  |
|  |  | BN1 - BN2 | 7 | 36 | 16 |  |
|  |  | BN2 - BN3 | 5 | 13 | 8 |  |
|  |  | BN3 - BN4 | 8 | 29 | 29 | 1 |
|  |  | BN4 - BN5 | 5 | 28 | 26 |  |
|  |  | BN5 - BN6 | 5 | 8 | 7 |  |
|  |  | Total | 35 | 121 | 92 | 1 |

BN = Block net		BUT = Bull trout		BKT = Brook trout	Hybrid = Bulltrout/brook trout

Night Snorkel Spearing

The bull trout intergrade zone encompassed five reaches; block net 6 through 11.  Each reach was approximately .2 miles in length.  All habitat types that allowed facemask access were snorkeled.  Night snorkel spear activities were conducted by using a dry suit, dive light, and sling spear.  Sling spears were constructed from 600 mm long by 19 mm diameter PVC pipe, tipped with a five prong frog gig, and used 9.5 mm latex tubing for the sling.  The sling spears were improved upon by tipping with a five-prong frog gig instead of the trident frog gig used in 1996.  Initially, it was thought that greater improvement of the spear design used in 1996 was necessary, but the five-prong frog gig used in 1997 improved spearing effectiveness dramatically.  Fish generally held still long enough when illuminated by a dive light to allow at least one (and sometimes more) good spearing attempt to be made.  From block net six to block net eleven 10 brook trout and 8 hybrids were removed.  A total of 54 bull trout were observed.

Night snorkel spearing data for Threemile Creek activities, 1997

|  |  | Reach | # Passes | BUT | BKT | Hybrid |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | BN6 - BN7 | 5 | 5 | 6 | 1 |
|  |  | BN7 - BN8 | 4 | 14 | 1 | 1 |
|  |  | BN8 - BN9 | 5 | 10 | 2 | 3 |
|  |  | BN9 - BN10 | 5 | 12 | 1 | 3 |
|  |  | BN10 - BN11 | 3 | 13 | 0 | 0 |
|  |  | Total | 22 | 54 | 10 | 8 |

BN = Block net		BUT = Bull trout		BKT = Brook trout	Hybrid = Bulltrout/brook trout

Discussion

Previous suppression activities conducted on Threemile Creek in 1996 revolved around members of the Working Group volunteering their time to assist in removal efforts.  Although suppression efforts were considered to be successful, the Working Group realized that they were not able to provide the time and energy necessary to continue removal activities on a yearly basis.  NFWF funding for a seasonal in 1997 allowed activities to be conducted on Threemile Creek more intensely and consistently than in 1996.

The following table provides the data collected for both 1996 and 1997

|  |  | Threemile Creek | BUT observed | BT removed (speared) | Hybrids removed (speared) | BT removed (shocked) | Hybrids removed (shocked) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 1996 | 21 | 27 | 8 | 616 | 12 |
|  |  | 1997 | 54 | 10 | 8 | 122 | 1 |

Electrofishing and night snorkel spearing activities appear to be effective in suppressing brook trout and hybrids in Threemile Creek.  Suppression efforts two years in a row show a decline in brook trout removed from both the brook trout electrofishing and bull trout intergrade zones.  Hybrid numbers removed in the brook trout zone for both years also show a decline.  The number of hybrids removed in the bull trout intergrade zone has however remained the same.  This can in part be attributed to more intensive suppression activities in 1997 and possible brook trout movement between 1996 and 1997 suppression activities.  In addition, activities conducted in 1997 doubled the minimum number of observed bull trout in Threemile Creek.  The greater number of bull trout observed is attributed to the intensity and consistency of activities applied to surveys in 1997.  Although bull trout numbers are still extremely low, the new number of existing bull trout improves the chances of successful recovery.

GPS Documentation:

Seeps and cold water springs in Threemile Creek brook trout removal area were located by ODFW using a Geo-Explorer I GPS unit.  The documentation of these seeps and springs is necessary for antimycin application if chosen as an alternative by the Working Group.  In addition Larry Dunsmoor from Klamath Tribes conducted intensive GPS work locating large woody debris, distribution, and block net sites in the Brook trout removal area.  Documentation of GPS work will be forthcoming.

Temperature:

Winema National Forest assisted removal efforts by placing temperature-monitoring devices throughout the Threemile Creek project area.  We hope to be able to describe the thermal characteristics of the stream above and below bull trout occupied habitat.  Results of temperature data will be forthcoming.

Macroinvertebrate Surveys:

Macroinvertebrate surveys were conducted on Threemile Creek Sept. 3, 1997 by Brian Quick (ODFW) and Jamie Greenstein (USFW).  Macroinvetebrate survey protocol and training was provided by Tom Friedrichson (Fremont National Forest).  Surveys were completed at 4 sites from 75 m below the culvert (barrier) at the 110 road crossing to 100m above the upper distribution of bull trout.  At each site (riffle, not less than 30m), samples were taken and stored in 80% ethanol. Macroinvertebrate samples will be analyzed by outside source for species composition.  Water samples were also taken and delivered to Tom Friedrichson (Fremont National Forest).  Tom will analyze water samples for alkalinity and sulfate content.  In addition, the following measurements were also taken at each sample site using a hydrolab supplied by USBOR: DO, CFS, pH, temperature (air & water), and conductivity.  The objective of the survey was to begin collecting data for NEPA documentation necessary for including antimycin as an alternative for exotic fish removal.

Amphibian Survey:

Amphibian surveys were conducted on Threemile Creek, early Sept. 1997, by ODFW personnel Brian Quick and Lori Lahoda.  Tom Friedrichson from Fremont National Forest provided amphibian protocol and survey training. Survey conducted utilized the visual encounter method.  Surveys were conducted during the day by walking both sides of the creek.  Pacific tree frogs were the only amphibian observed. The objective of this survey was to begin collecting data for NEPA documentation necessary for including antimycin as an alternative for exotic fish removal.

Trapping Effort:

Traps were designed in an effort to collect fish to aid in the removal of brook trout and identification of other species including bull trout adults and fry.  Traps were designed from various types of materials including 2-6 inch PVC pipe and ¼ inch mesh wire, some covered by fine screen door mesh.  Traps were placed in various places in Threemile and Cherry creeks, including small and large pools and some deeper riffles.  Traps were set during the month of July 1997.  Different types of bait were used in the traps including cat food, powerbait, and Velveeta cheese. Bait was placed in small, perforated tubes in the bottoms of the traps.  Photos were taken of the traps before being placed in the creeks and some underwater photography was done once traps were set.

No fish were collected in any trap during the effort.  The Working Group hoped that trapping might be an available alternative for the removal of exotic fish species.  Unfortunately, trapping at this time does not look like a viable alternative.  However, we have not given up on trapping as a method in which to remove exotic fish species.  Design changes will be made during the winter months and efforts will resume in the spring.

1.  Reduce non-native brook trout’s competitive and genectic interaction with bull trout.

2.  Quantify the number of brook tortu removed.

3.  Improve spearing efficiency for brook trout in the intergrade zone.

4.  Develop effective trap designs and innovative approaches for removal of brook trout in the intergrade zone.

5.  Provide information that could be transferred to other phase I activities within the Klamath Basin and share with other bull trtou working groups.

6.  Create a picture library of genectically pure trout versus hybrids.

7.  Obtain data on existing macrtoinvertebrate, mollusc, and amphibian populaitons.