The Effects of Villwok’s

Ford on Native and Exotic Fishes of Rickreall Creek

Prepared

In fulfillment of Requirements for FW 441, 442, &443

For

Department of Fisheries and Wildlife, Oregon State University

&

The Rickreall Watershed Council

By

Russell Chapman, Francis Drake, Brian Hawkins, Shawn Woods, & Garth Wyatt

Instructed by Douglas Markle, Ph.D.

Table of Contents

- Executive Summary

- Introduction

  - Rickreall Creek and Villwok’s Ford background information

- Methods

  - Hydrological

  - Biological

  - Culvert Analysis

  - Ford Analysis

  - Discharge and Culvert Timing

  - Swimming Abilities

  - Temperature Limits

- Results

  - Culvert Analysis

  - Ford Analysis

    - Discharge

    - Water Velocity

    - Temperature

- Figures and Tables

  - Figures

  - Tables

- Discussion

  - Villwok’s Ford

  - Policies

- Acknowledgements

- References

  - Works cited

  - Bibliography

- Illustrations

  - Maps

  - Photographs

- Appendix

  - Culvert analysis graphs

1.0 Executive Summary

- Previous studies observed introduced Centrarchids (bass, bluegill) only below Villwok’s Ford, yet introduced coho salmon throughout the main-stem of Rickreall Creek.

- Villwok’s ford brings two distinct aspects to the issue of fish passage.

  - During low flows (below 45 cfs) water will flow only through the culvert.

    - Generally May through November

  - During high flows (above 45 cfs) water will flow over the ford creating a spillway.

    - Generally November through May

- Culvert dynamics on fish passage

  - Passage by adult salmon and steelhead under most conditions.

  - Other species had violations by Fish-Xing (stream simulation software program) parameters;

    - Depth vs. discharge

    - Leap velocity vs. discharge

    - Water velocity vs. discharge

- Spillway dynamics on fish passage

  - Adult salmon and steelhead able to exceed observed water velocities, and ford jump height on all dates (February-May).

  - Centrarchids and juvenile salmonids are not able to pass due to velocity, and/or jump height.

  - Adult suckers and cutthroat able to pass on all visits from February-May, except April 11th due to velocity

- Violates ODFW Policy on barriers for all species at some life history stage

2.0 Introduction

Rickreall Creek is a 4th order tributary of the Willamette River in Polk County, Oregon (Mattson and Gallagher 2001). Previous fish sampling had indicated a high percentage of exotic fishes in the lower portion of the creek (Altman 1997) and in an upstream reservoir (Chastain et. al. 2002). However, within the mainstem, exotic fishes (with the exception of planted juvenile coho) are absent above Villwok’s Ford, the lowermost barrier on the creek at about river km 12.7 (Chastain et. al. 2002). A 1995 CH2MHill survey noted the ford was a culvert and not passable while Mattson and Gallagher (2001) found water flowing over the ford and fish passage “appeared possible”. Because the ford appears to violate Oregon statutes regarding fish passage at man-made barriers, but may paradoxically provide benefits by excluding exotic fishes, we initiated a study of the ford and of a variety of fishes to determine the seasons and conditions during which the ford was a barrier to fish passage.

2.1 Rickreall Creek and Villwok’s Ford

According to Mattson and Gallagher (2001) there are twenty five fish species suspected to inhabit Rickreall Creek and its tributaries (Table 11).  Thirteen are native species and twelve have been introduced.  Currently coho are the only introduced fish in the mainstem that has been observed above Villwok’s Ford with the exception of largemouth bass in Mercer Reservoir at river km 39.4 (Chastain et. al. 2002).  However, Mattson and Gallegher (2001) found eight other exotics in the watershed.

Species found in the mainstem of Rickreall Creek that migrate to and from the Willamette River are the anadromous fishes: coho, chinook, steelhead, cutthroat, and Pacific lamprey (Hart 1980).  Large scale suckers, although not anadromous, also migrate to and from the Willamette River.  It is understood that catostomatids inhabiting rivers ascend smaller streams for spring spawning (Curry and Spacie 1984).

Villwok’s Ford was built in the late 1950s or early 1960s, replacing a bridge previously located directly downstream.  Currently, the ford is used by farmers to transport farm equipment to isolated fields south of Rickreall Creek.  The Ford is located at river km 12.74 (Chastain et. al. 2002) on Rickreall Creek near Rickreall Oregon.  It is approximately 9.79 river km downstream from Dallas City Park located in Dallas which is the largest town on the stream.  The ford is a concrete structure that is partially hollow and has been built up over the years when needed.  It is 36.9 meters long and 5.3 meters wide from downstream lip to upstream lip.  The culvert located within Villwok’s Ford is a concrete oval tube with dimensions: 0.67 meters high, 0.60 meters wide and 4.7 long.  It is constructed of non-corrugated concrete and has a slope of 2.34 percent.

Villwok’s Ford is dynamic, since part of the year water flows only through the culvert and during the rest of the year water flows through the culvert and over the ford, acting as a spillway.  It is a culvert during low flow, approximately May-November, and is a spillway during high flows, approximately November-April, (USGS 14190700).

3.0 Methods

We collected hydrological, biological and temperature data at Villwok’s Ford and compared these variables to long-term discharge and velocity in order to determine the approximate time period discharge levels would allow for upstream fish passage.  Data was collected at least once a month from February 2003 to October 2003.  We gathered the data using basic tools such as a measurement tape, thermometer, velocity meter, global positioning satellite receiver (GPS) and stadia rod.

3.1 Hydrological

We measured cross-sectional profiles of water depth and velocity across the stream at three transects.  Cross sections were located ten meters upstream of the ford, on the ford, and one meter below the ford.  Cross sectional profiles were measured from March to June, as the water was flowing over the ford.  At all three locations the wetted width and water depth were measured every half-meter.  We took velocity measurements at four equidistant locations across the wetted width on the upstream and ford transects.  The position at which velocities were measured below the ford was variable between dates in order to represent the variation in velocity.  Water velocity measurements were taken within sections of approximately homogenous flow.  We used a calibrated propeller driven flow meter to record velocity over two minutes (Table 8).  The flow meter was a model 005WA200 made by Kahl Scientific Instrument Corp.

From June to October, when stream discharge was low and only flowing through the culvert, the procedure was altered.  Maximum water depth and three velocity measurements were taken at the culvert inlet and outlet.

We preformed a temperature profile of the Creek in October to understand temperature regime along the creek. Ten roughly equidistant sites were chosen from river km 0.56 to 30.0.  At each sampling and/or data gathering at the ford or mouth, water temperature was also noted.

3.2 Biological

Fish composition and distribution in Rickreall Creek was described by Chastain et. al. (2002) and Mattson and Gallagher (2001).  We conducted a more detailed survey in the vicinity of the ford to confirm distribution patterns found in past studies and to better understand seasonal fish movement.  From May to September snorkel surveys and seining were performed at least once a month.

We conducted a literature review to determine conditions and seasons when the ford would be a barrier to fishes.  When available, we obtained: spawning temperatures and dates, swimming performances, minimum landing water depths and jump height abilities.  We were able to gather some or all of these data for juvenile and/or adult coho, chinook, steelhead, rainbow, sucker, largemouth bass, bluegill, and longear sunfish.

3.3 Culvert Analysis

A USFS stream simulation software program (Fish Xing 2001) was the primary tool for determining passage during culvert flow situations.  This software evaluates whether or not the culvert was passable by a given species/life history stage.  It uses culvert installation data, biological and physiological data, and a series of design flows of 2, 25, and 40 cubic feet per second (cfs).  Culvert installation data included culvert type, material, installation style, length, percent slope, roughness coefficient of construction material, inlet elevation, outlet elevation, and inlet head loss coefficient.  Biological data included species information, fish length, minimum water depth, migration period, prolonged swimming speed, prolonged time to exhaustion, burst swimming speed, burst time to exhaustion, and jumping speed.  Three comparisons were made for three different discharge scenarios, by species and life history stage.  The three comparisons were: minimum leap velocity vs. discharge, water depth in culvert vs. discharge, and water velocity vs. discharge.  The software calculated whether low passage flow, high passage flow, insufficient depth, excessive velocity, excessive leap velocity, or shallow pool depth prevented passage for the species present.

3.4 Ford Analysis

The hydrological and biological data were used to determine passage ability.

3.5 Discharge and Culvert Timing

Twenty years of USGS discharge readings from station 14190700, at the mouth of Rickreall Creek were used to estimate the time of culvert flow and over-ford flow.  The twenty-year average daily discharges were then compared to the capacity of the culvert (45 cfs) in Villwok’s Ford, to estimate seasons when discharge would overflow the ford.

3.6 Swimming Abilities

Swimming abilities of seven species and two life history stages (adult and juvenile) (Kolok 1992; Bell 1973, 1991; Bjornn and Reiser 1992) were compared to cross-sectional velocities one meter downstream of the edge of the ford on each sampling date.

3.7 Temperature Limits

Daily average temperatures were calculated from 1991 data collected at the mouth of Rickreall Creek (USGS 11102).  These daily average water temperatures were used to determine conditions present while centrarchids might be spawning.  Temperature readings at Dallas City Park from 2001-2002 (Chastain et. al. 2002) were also used to evaluate conditions present above Villwok’s Ford.

4.0 Results

4.1 Culvert Analysis

Fish Xing analysis of the culvert indicated that adult salmonids were the only species/life history stage able to pass at all discharges between 2 and 40 cfs.  All other species/life history stage had a violation of at least one comparison of depth vs. discharge, leap velocity vs. discharge, or water velocity vs. discharge (Appendix).  If one of these violations occurred passage was not allowed.  We have constructed tables to determine whether or not a given species of fish is able to pass through the culvert. There is a table for each of the following discharge levels, 2, 25, and 40 cfs. The tables include the results of the three calculated relationships of depth in culvert vs. discharge, discharge into the culvert vs. velocity generated by discharge, and minimum leap velocity vs. discharge. If one of these relationships is violating the fish’s ability to swim then the culvert is deemed a barrier for passage. Adult coho and steelhead are the only species/life history stages that are predicted to pass at 2 cfs (Table 1).  All fish are unable to pass at 25 cfs except adult salmon and steelhead (Table 2).  Adult chinook and steelhead were again the only species/life history stage predicted to pass the culvert at 40 cfs, excluding all others from upstream passage (Table 3).

4.2 Ford Analysis

4.2.1 Discharge

The discharge of Rickreall Creek varies greatly from year to year (Fig. 1).  Minimum summer discharges have approached zero on several years, and peak flows have been as large as 5650 cfs of water (Table 4).  This twenty-year record of discharge at the mouth of Rickreall Creek is a fairly good predictor of when the stream is flowing over the ford (November to May) and when it is confined to the culvert (May to November) (Fig. 2).

Based on Fish X-ing program’s calculations, the culvert in Villwok’s Ford can only accommodate 45 cfs of water.  Our observations are consistent with this prediction when the twenty-year average discharge is applied at the ford. All of the dates that the stream was confined to the culvert are below the 45 cfs line, thus the period when the culvert is active is estimated to be between May and November (Fig. 2).

On October 24th 2003, when the discharge was less than 45 cfs, a board was placed in front of the culvert intake which caused flow over the ford.

4.2.2 Water Velocity

The swimming abilities of seven species and two life history stages (adult and juvenile) were compared to the observed water velocities below the ford.  Adult salmon and steelhead were the only fish that were able to exceed observed water velocities on all dates, thus being able to pass on a velocity basis (Table 5).  Both of the centrarchid species (juvenile largemouth bass and sunfish) and the juvenile salmonids (rainbow trout and juvenile chinook and coho salmon) present in the stream would not be able to pass some portion of the ford on a velocity basis from February to May.  Adult suckers and cutthroat trout would have been able to exceed water velocities present on all visits except April 11th.

The jump heights of various fish also limit their ability to pass the ford.  Adult chinook, coho, and steelhead are capable of jumping heights in excess of 2.1 meters (Bjornn and Reiser 1992).  This jump height is well over the 1.17 meter height of the ford and depth of water required for landing was adequate, which would allow for upstream passage from February to April.  This is a moot point, however; chinook and coho salmon are expected to be migrating from November to January (Kahler and Quinn 1998) (Table 6).  Data were recorded for only one month of winter steelhead’s migration period, February.

The value for the minimum water depth required for landing from a jump is 0.24m for chinook, 0.18m for steelhead, and 0.12m for sucker adults (Fish Xing 2001).  The depths present across the ford were sufficient for Chinook and steelhead except near the fish ladder during the February visit, which is during the expected time of migration use by steelhead.  During the period of expected migration use by suckers (early spring), landing depths were sufficient except near the fish ladder as well.

The maximum jumping ability of bluegill is 0.76 meters which is considerably less than the height needed to clear the ford (Ellis 1974).  This jump may be possible at higher discharges; however the velocities present would be in excess of their swimming ability during over-ford flows, prohibiting upstream passage.

Villwok’s Ford is at least a partial barrier to Pacific lamprey, since they are unable to negotiate fish ladders (Mattson and Gallegher 2001).  This is likely due to the rough nature of concrete which is not conducive to suction by a lamprey’s oracle.

4.2.3 Temperature

The temperature regime in Rickreall Creek does vary upstream from the mouth. However, the temperatures do not vary as a function of river km upstream, so temporal and spatial estimates of temperatures are not possible with available data.

Temperatures at the mouth and ford were observed to differ less than 5 Celsius degrees on any date in 2001-2002 (Chastain et al. 2002) (Table 4).  The role of temperature does not seem to be that important in limiting the distribution of centrarchids in Rickreall Creek.  Since the temperatures present at the mouth are close to those present at the ford, conditions for centrarchids to spawn should be present.  Additionally if bluegill and largemouth bass were able to pass the ford, they would likely be able to spawn in the area of the Dallas City Park, if temperatures are similar to those recorded in 2001-2002 (Table 7).  This would result in the expansion of their known distribution in Rickreall Creek by 9.8 river km (Table 9) (Chastain et. al. 2002; Personal findings).

# 4.3 Biological

4.3.1 Results Snorkeling and Seining

The snorkeling and seining surveys done during our project support past findings of species distribution along Rickreall Creek.  One of the few differences between our observations and Chastain et. al. (2002) is that no largemouth bass were encountered and Northern pike minnow were encountered upstream of the ford (Table 10).  In the Fishes of Rickreall Creek report (Chastain et al. 2002) bass were caught below the ford and no pike minnow were captured above the ford.

5.0 Figures and Tables

5.1 Figures

Fig. 1: Variation in discharge [log(cfs)] over twenty years compared to the log(20-year average discharge) measured at the mouth of Rickreall Creek.  Black lines are the years from 1958 to 1977, and the orange line is the 20-year average (USGS 14190700).

Fig. 2: Culvert timing determined by the twenty-year average discharge compared to the culvert’s discharge capacity (cfs), and each of the dates sampled denoted in green (USGS 14190700).

Fig. 3: Observed centrarchid spawning times and temperatures compared to temperatures at the mouth of Rickreall Creek in 1991 (Eaton and Scheller 1996; Emig 1966; Miller and Kramer 1971; Morgan 1951; Moyle 1976; USGS 11102)

Fig. 4: Observed 2001-2002 temperatures at Dallas City park compared to observed Bluegill and Largemouth bass spawning times and temperature range. (Chastain et al. 2002; Eaton and Scheller 1996; Emig 1966; Miller and Kramer 1971; Morgan 1951; Moyle 1976).

5.2 Tables

Table 1:  Prediction of passage by fish species and life history stage at Villwok’s Ford based on depth, velocity, or minimum leap velocity at 2 cfs.  Results from Fish Xing.

| 2 CFS |  |  |  |
| --- | --- | --- | --- |
| Species | Depth in Culvert vs. Discharge | Discharge vs. Velocity | Minimum Leap Velocity Vs. Discharge |
| Chinook Adult | No | Yes | Yes |
| Chinook juvenile | Yes | No | No |
| Coho Adult | Yes | Yes | Yes |
| Coho juvenile | Yes | No | No |
| Cutthroat Adult | Yes | Yes | No |
| Rainbow Adult | Yes | No | No |
| Sucker Adult | Yes | Yes | No |
| Longear Sunfish | Yes | No | No |
| Steelhead Adult | Yes | Yes | Yes |
| Steelhead Juvenile | Yes | No | No |

Table 2: Prediction of passage by fish species and life history stage at Villwok’s Ford based on depth, velocity, or minimum leap velocity at 25 cfs.  Results from Fish Xing.

| 25 CFS |  |  |  |
| --- | --- | --- | --- |
| Species | Depth in Culvert vs. Discharge | Discharge vs. Velocity | Minimum Leap Velocity Vs. Discharge |
| Chinook Adult | Yes | Yes | Yes |
| Chinook juvenile | Yes | No | No |
| Coho Adult | Yes | Yes | Yes |
| Coho juvenile | Yes | No | No |
| Cutthroat Adult | Yes | No | No |
| Rainbow Adult | Yes | No | No |
| Sucker Adult | Yes | No | No |
| Longear Sunfish | Yes | No | No |
| Steelhead Adult | Yes | Yes | Yes |
| Steelhead Juvenile | Yes | No | No |

Table 3: Prediction of passage by fish species and life history stage at Villwok’s Ford based on depth, velocity, or minimum leap velocity at 40 cfs.  Results from Fish Xing.

| 40 CFS |  |  |  |
| --- | --- | --- | --- |
| Species | Depth in Culvert vs. Discharge | Discharge vs. Velocity | Minimum Leap Velocity Vs. Discharge |
| Chinook Adult | Yes | Yes | Yes |
| Chinook juvenile | Yes | No | No |
| Coho Adult | Yes | Yes | No |
| Coho juvenile | Yes | No | No |
| Cutthroat Adult | Yes | Yes | No |
| Rainbow Adult | Yes | No | No |
| Sucker Adult | Yes | No | No |
| Longear Sunfish | Yes | No | No |
| Steelhead Adult | Yes | Yes | Yes |
| Steelhead Juvenile | Yes | No | No |

Table 4: Minimum and Maximum discharge (Q) for each of the twenty years of gauge records at the mouth of Rickreall Creek (USGS 11102).

| Year | Minimum Q(cfs) | Maximum Q(cfs) |
| --- | --- | --- |
| 1958 | 0.7 | 2420.0 |
| 1959 | 0.58 | 1910.0 |
| 1960 | 1.9 | 2290.0 |
| 1961 | 0.57 | 1100.0 |
| 1962 | 0.44 | 1790.0 |
| 1963 | 1.2 | 2330.0 |
| 1964 | 0.01 | 3430.0 |
| 1965 | 2.7 | 2440.0 |
| 1966 | 3.6 | 3560.0 |
| 1967 | 3.2 | 2900.0 |
| 1968 | 0.2 | 1120.0 |
| 1969 | 4.3 | 1240.0 |
| 1970 | 2.4 | 3700.0 |
| 1971 | 3.8 | 625.3 |
| 1972 | 0.8 | 1900.0 |
| 1973 | 1.4 | 3180.0 |
| 1974 | 1.9 | 1690.0 |
| 1975 | 2.0 | 1720.0 |
| 1976 | 2.2 | 1780.0 |
| 1977 | 1.7 | 5650.0 |

Table 5: Maximum burst speed (m/s) by species and life history stage and the percent of the wetted width of the stream that was impassible on that date (Kolok 1991; Bell 1973,1991; Bjornn and Reiser 1992).

|  |  | % Impassible |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Species | max burst (m/s) | 6-Feb | 1-Mar | 11-Apr | 27-Apr | 9-May |
| Bass J | 0.31 | 58 | 39 | 53 | 54 | 83 |
| Sunfish | 0.65 | 58 | 36 | 44 | 54 | 47 |
| Chinook A | 6.83 | 0 | 0 | 0 | 0 | 0 |
| Chinook J | 0.34 | 58 | 39 | 47 | 80 | 54 |
| Coho A | 6.55 | 0 | 0 | 0 | 0 | 0 |
| Coho J | 0.34 | 58 | 39 | 47 | 80 | 54 |
| Steelhead | 8.08 | 0 | 0 | 0 | 0 | 0 |
| Rainbow J | 1.5 | 6 | 12 | 44 | 17 | 33 |
| Cutthroat A | 2.4 | 0 | 0 | 39 | 0 | 0 |
| Sucker A | 2.1 | 0 | 0 | 39 | 0 | 0 |

Table 6: Time of use for migration, spawning, or residency, by species and life history stage (Kahler and Quinn 1998).

| Species | Use Period |
| --- | --- |
| Steelhead | November to February |
| Coho A | November to January |
| Coho J | >1 yr. residency to smolt |
| Chinook A | November to January |
| Chinook J | >1 yr. residency to smolt |
| Bass A | spawn April to June |
| Bluegill | Summer spawn |

Table 7: Difference in temperatures at the mouth and Dallas City Park in 2001-2002 (Chastain et al. 2002).

| Date | Tmouth | Tford | Tdallas | Tmouth –Tdallas |
| --- | --- | --- | --- | --- |
| 28-Apr | 11.8 | 13.2 | 9.5 | -2.3 |
| 18-May | 14.0 | 12.0 | 12.0 | -2.0 |
| 23-Jun | 16.1 | 19.0 | 17.0 | 0.9 |
| 14-Jul | 19.5 | - | 19.0 | -0.5 |
| 18-Aug | 19.0 | 20.0 | 17.0 | -2.0 |
| 8-Sep | - | - | 15.5 | - |
| 12-Oct | 12.5 | 17.5 | 11.0 | -1.5 |
| 3-Nov | 18.0 | 19.0 | 17.0 | -1.0 |
| 9-Dec | 19.0 | 19.0 | 19.0 | 0.0 |
| 13-Jan | 6.5 | 6.5 | 7.0 | 0.5 |
| 10-Feb | 6.0 | 5.5 | 5.5 | -0.5 |
| 10-Mar | 6.5 | 6.5 | 6.0 | -0.5 |

Table 8: Trial number, meters traveled, number of revolutions, and meters/revolution used to calibrate the velocity meter in order to obtain a conversion factor for revolutions to meters per second.

| Trial # | Meters traveled | Revolutions | Meters/revolution |
| --- | --- | --- | --- |
| 1 | 25 | 123 | 0.203252033 |
| 2 | 25 | 100 | 0.250000000 |
| 3 | 25 | 122 | 0.204918033 |
| 4 | 25 | 129 | 0.193798450 |
| 5 | 25 | 118 | 0.211864407 |
| 6 | 25 | 142 | 0.176056338 |
| 7 | 25 | 132 | 0.189393939 |
| 8 | 25 | 129 | 0.193798450 |
| 9 | 25 | 140 | 0.178571429 |
| 10 | 25 | 135 | 0.185158185 |
| 11 | 25 | 130 | 0.192307692 |
| 12 | 25 | 135 | 0.185185185 |
| 13 | 25 | 147 | 0.170068027 |
| 14 | 25 | 133 | 0.187969925 |
| 15 | 25 | 141 | 0.177304965 |
| 16 | 25 | 141 | 0.177304965 |
| 17 | 25 | 141 | 0.177304965 |
| 18 | 25 | 139 | 0.179856115 |
| 19 | 25 | 143 | 0.174825175 |
| 20 | 25 | 145 | 0.172413793 |
| Conversion factor=0.18117m/revolution |

Table 9: Site name and river km upstream from the mouth of Rickreall Creek (Chastain et al. 2002)

| Site Name | River km |
| --- | --- |
| RV Park | 0.56 |
| White’s | 10.06 |
| Villwok’s Ford | 12.47 |
| Al’s Hole | 15.18 |
| Dallas City Park | 22.26 |

Table 10:  Summary of relevant species caught by snorkeling and/or seining downstream and upstream of Villwok’s Ford from May through September 2003.

| Downstream of ford |
| --- |
| Species | May 23 | June 1 | June 6 | June 27 | July 12 | July 26 | Aug. 18 | Sept. 6 |
| Ptychocheilus oregonensis | No | Yes | No | Yes | Yes | Yes | Yes | No |
| Lepomis spp. | No | No | Yes | Yes | Yes | Yes | Yes | Yes |
| Oncorhynchus clarki | Yes | Yes | No | No | Yes | Yes | Yes | Yes |
| Catostomus machrocheilus | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Lampetra tridentata | No | Yes | No | No | No | No | No | No |
| Upstream of ford |
| Ptychocheilus oregonensis | No | No | No | No | No | No | Yes | No |
| Lepomis spp. | No | No | No | No | No | No | No | No |
| Oncorhynchus clarki | Yes | No | No | No | No | Yes | No | No |
| Catostomus machrocheilus | Yes | Yes | Yes | No | Yes | Yes | No | Yes |
| Lampetra tridentata | No | No | No | No | No | No | No | No |

Table 11: Fish species thought to occur in Rickreall Creek and its tributaries (Mattson and Gallegher 2001).

| Fish species thought to occur in Rickreall Creek and its tributaries |
| --- |
| Native species | Introduced species |
| Common Name | Scientific name | Common name | Scientific name |
| cutthroat trout | Oncorhynchus clarki | coho salmon1 | Oncorhynchus kisutch |
| steelhead | O. mykiss | brown trout1 | Salmo trutta |
| chinook salmon1 | O. tshawytscha | warmouth sunfish1 | Lepomis gulosus |
| Pacific lamperey1 | Lampetra tridentate | bluegill sunfish1 | L. macrochirus |
| western brook lamprey | L. richarsoni | pumpkinseed1 | L. gibbosus |
| speckled dace | Rhinichthys osculus | brown bullhead1 | Ameiurus nebullosus |
| northern pike minnow | Ptychocheilus oregonensis | mosquitofish1 | Gambusia affinis |
| largescale sucker | Catostomus macrocheilus | yellow perch1 | Perca flavescens |
| redside shiner | Richardsonius balteatus | smallmouth bass | Micropterus dolomieui |
| reticulate sculpin | Cuttus perplexus | largemouth bass | M. salmoides |
| torrent sculpin | C. rhotheus | white crappie1 | Pomoxis annularis |
| sandroller1 | Percopsis transmontana | black crappie1 | P. nigromaculatus |
| Oregon chub1 | Oregonichthys crameri |  |  |

1 Thought to occur infrequently.

Table 12:  Fish species observed in mainstem Rickreall Creek (Chastain et.al. 2002).

*not found upstream of Villwok’s Ford

| Native species | Introduced species |
| --- | --- |
| Common name | Scientific name | Common name | Scientific name |
| Northern pike minnow | Ptychocheilus oregonensis | Coho salmon | Oncorhynchus kisutch |
| Redside shiner | Richarsonius balteatus | Pumpkinseed* | Lepomis gibbosus |
| Speckled dace | Rhinichthys osculus | Bluegill* | L. macrochirus |
| Chiselmouth | Acrocheilus alutaceus | Largemouth bass* | Micropterus salmoides |
| Peamouth | Mylocheilus caurinus |  |  |
| Largescale sucker | Catostomus macrocheilus |  |  |
| Torrent sculpin | Cottus rhotheus |  |  |
| Reticulate sculpin | C. perplexus |  |  |
| Riffle sculpin | C. gulosus |  |  |
| Prickly sculpin | C. asper |  |  |
| Chinook salmon | Oncorhynchus tshawytscha |  |  |
| Cutthroat trout | O. clarki |  |  |
| Steelhead/rainbow trout | O. mykiss |  |  |
| Pacific lamprey | Lampetra tridentata |  |  |
| Threespine stickleback | Gaterosteus aculeatus |  |  |
| Sandroller | Percopsis transmontana |  |  |

### 6.0 Discussion

6.1 Villwok’s Ford

There is a large amount of variability in many of the environmental factors influencing fish passage at Villwok’s Ford.  Discharge can range from near zero during the summer months to as high as 5600 cfs.  The timing of when the stream is confined to the culvert and when it is flowing over the ford is influenced by discharge, but without human management, the scenario would be much different.  The ability of a fish to pass the ford is very much dictated by the activities of people.

The degree to which local people play a role in the dynamics and fish passage ability of Villwok’s ford is high.  Since the natural state of the stream has been altered, maintenance and manipulation of the ford/culvert is an important factor in allowing upstream fish passage.  Without Mr. Joslin clearing the culvert inlet of bed-load, it would likely stay clogged.  The involvement of the Polk County Sportsmen’s Club (PCSC) also plays a role in the upstream movement of fish, primarily coho salmon.

In the late 1980s the Polk County Sportsmen’s Club built a fish box (like a fish ladder) on the north side of the ford to improve fish passage.  Annually, around mid-October, members of the Sportsmen’s Club block the culvert and place boards in the river above the ford to divert flow to the fish box.  The timing of this coincides with the returning migration of spawning coho.  The culvert remains blocked with bed-load throughout the winter, forcing water to flow over the ford.  During November 2003, the PCSC worked to aide fish passage by making improvements to the fish box.  They did this by increasing the height of the sides and adding structure along the downstream edge of the ford.

Jason Duncan of the PCSC has shared information about salmon being observed passing the ford on their way upstream to spawn.  Mr. Duncan has talked to a biologist who believes that three adult salmon they were observing swam up through the culvert when the water was low.  When conditions did not allow passage at all, he has seen coho spawn directly downstream of the ford.  In 2002 he observed approximately 100 redds below the ford.  This is the reason that the PCSC has intervened by placing boards across the ford in order to divert water to the fish box from October through December 15th.  Mr. Duncun has also seen juvenile chinook salmon move upstream in December and stop below the ford.

The PCSC wants the City of Dallas to release more water from Mercer Dam (near the head-waters of Rickreall Creek) during crucial coho migration and spawning times.  The Sportsmen’s Club would like to improve fish passage by making a more gradual step-cline fish ladder and create deeper pools at the downstream edge of the ford to promote upstream movement.  They also think that carving out a small channel in the ford above the fish box would increase flow to the fish box and provide a greater landing depth for the fish to swim over the ford.

This may be an adequate solution to the adult salmonid passage issue, but due to the lack of data on other species’ (i.e. sculpins, minnows, and sandrollers) swimming abilities and movement patterns, Villwok’s Ford may continue to be a barrier.

From February to May the ford was a barrier to juvenile salmonids.  The water velocities observed at the ford also exceeded the swimming abilities of bluegill and juvenile largemouth bass from February to May.  It is possible that centrarchids are in the upstream reaches of Rickreall Creek.  A local resident, and member of the PCSC, informed us that he saw a “pan fish” and some largemouth bass near the Dallas reach of Rickreall Creek about fifteen years ago.

In Rickreall Creek there are many other species of fish. There are four sculpin species (Cottidae) and five minnow species (Cyprinidae) that occur both upstream and downstream of the ford.  If these groups of fish are unable to move past the ford, these populations are, in effect, cut-off or fragmented from each other.  Downstream movement by these species may be possible if they are washed over the ford or through the culvert.  However, is likely that they will not be able to move back upstream.  During high flows, fish may be swept downstream if adequate refuge is not present.  The impediment to upstream movement may result in a change in species composition and/or abundance.

One interesting discovery below the ford was a dead Pacific lamprey and two redds within three meters of the lamprey.  We could not conclusively identify that the redds were created by the lamprey but this was the only day a lamprey or any redds were observed by our group.  Additionally, the proximity of the two in conjunction with the shape of the redd led us to believe that they were created by a Pacific lamprey.  Chastain et. al. (2002) observed that most of the Pacific lamprey caught in their study were below the ford.  From what has been observed, the ford may limit their upstream movement (Table 10).  This species is being petitioned for listing as endangered under the federal Endangered Species Act and are currently a species of concern (Mattson and Gallegher 2001).

Our results for upstream passage ability may be on the conservative side.  Results from qualitative analysis such as those from Kane and Behlke (1986) all indicate that under certain conditions, fish are capable of exceeding velocities greater than those indicated by current culvert design guidelines.  They confirm the passage of juvenile coho salmon 50mm long through a 116 feet long culvert with a maximum slope of 5.3 percent.  This is a much steeper slope than that of the culvert in Villwok’s Ford, and passage was still possible.

The distributional expansion of introduced centrarchids is feasible if the ford were removed.  The introduction and spread of exotics is a cosmopolitan problem.  In Japan the introduction largemouth bass and bluegill has been shown to decrease, and in some cases cause local extinction of crustaceans, odonates, and fish (Maezono and Miyashita 2003).  Bluegill have also been observed to negatively influence growth/weight and behavior of native fish in California (Marchetti 1999).  The ecological implications of allowing exotics to expand their distribution should not to be overlooked.

The extent of the possible expansion of centrarchid distribution in Rickreall Creek would likely be limited to the City of Dallas, where the stream changes many of its characteristics.  The stream gradient becomes greater, and the amount of pool habitat decreases.  This would limit the expansion of bluegill, due to their preference of habitat types that contain greater than 60 percent pools (Wood 1995).

If the suggested plan from ODFW to remove Villwok’s Ford proceeds, there is a high probability that introduced exotic centrarchids will disrupt the ecology of Rickreall Creek above Villwok’s Ford.  If the ford is left in place in its current condition there are also concerns for upstream movement and historic species composition.  Perhaps allowing exotic centrarchids and coho to expand their distribution upstream to Dallas is the lesser of two ecological evils.

Villwok's Ford is a partial barrier to some fish, during some part of their life history.  It also appears to be the limiting factor in the distribution of exotic centrarchids in the mainstem of Rickreall Creek.  In order to form a more sound biological opinion, ecological studies that look at aspects of biodiversity, relative abundance, and behaviors of aquatic fauna up and downstream of Villwok’s Ford.

# 6.2 Policies

Whether or not Villwok’s Ford is a barrier to upstream fish passage is a complex issue.  Depending on the criterion, for an individual species or life history stage, the answer is different.  Different regulatory agencies have different criteria.  ODFW has a guideline that deems plunge heights of six inches for juveniles, and one foot for adults, impassible.  Additionally, the Canadian Department of Fisheries and Oceans has set the water velocity of 1.0 m/sec as a guideline for maximum velocity suitable for upstream fish passage, which is much less than swimming abilities obtained by our literature review.  These guidelines are useful for broad scale management uses, where detailed site-by-site analyses are not economically feasible.

Oregon Department of Fish and Wildlife (ODFW) are responsible for setting guidelines for fish passage in Oregon.  Other agencies such as U.S. Fish and Wildlife Service, Oregon Department of Forestry, National Oceanic and Atmospheric Administration, and the Environmental Protection Agency also have rules and regulations regarding fish passage.

Fish passage policies have been evolving for 150 years.  In Oregon, concern over fish passage is older than the state.  “When the Oregon Territory was established in 1848, its new constitution prohibited people from blocking salmon streams and specifically addressed the construction of fish passage facilities” (Bastasch 1998).  The most recent applicable legislation (HB 3002) was signed into law by Governor Kitzhaber in 2001 and was designed to merge existing statutes into one that was more flexible and “user-friendly” for all groups involved in fish passage issues.

The law created a council made up of interest groups/categories including water users, fish interests, and the general public. The law mandates fish passage both upstream and downstream at any man-made structure where migratory fish are present now or at any time historically.  The law also requires ODFW to conduct a statewide inventory of all artificial obstructions and their impacts on fish.  At present, all major, and a large percentage of minor, obstructions are inventoried.

The law also has provisions for owner/operators to apply for cost-sharing from ODFW if owners volunteer or if they are directed by the council to upgrade or change the obstruction.  The cost sharing allows owners to petition for up to 60% of upgrade costs.  This provision helps the owner/operator to become more proactive in the fish passage issue.

Variables of concern in the ODFW guidelines include the maximum velocities, minimum water depth, and jump pools along with jump heights into culverts (ODFW Fish Passage Program).  According to ODFW guidelines and this group’s findings the ford/culvert is in violation of fish passage requirements at least part of the year.  Consequently ODFW has slated Villwok’s Ford for removal, or renovation.

7.0 Acknowledgments

A special thanks goes out to Doug Markle, Dave Joslin,

Chad Woods, Jackie Hastings, Rickreall Watershed Council, Richard Schmitz, Oregon Watershed Enhancement Board, United States Forest Service, Gary Galovich, Andy and Bax Sporting Goods, Jason Duncan, Department of Fisheries and Wildlife Oregon State University.

Funding and supplies were made possible through the Polk Soil and Water Conservation District, Rickreall Watershed Council and Oregon State University.

8.0 References

8.1 Works Cited

Altman B., C. Benson, and I. Waite. Summary of information

on aquatic biota and their habitats in the Willamette

Basin, Oregon, through 1995. Water-Resources

Investigations Report 97-4023. U.S. Geological Survey

Portland, OR. 1997.

Bell, M. 1991. Fisheries Handbook of Engineering

Requirements and Biological Criteria, Portland,

Oregon: US Army Corps of Engineers, North Pacific

Division,.pp 1~1-	35~7.

Bjornn, T.C. and D.W. Reiser. 1992. Habitat requirements of 	salmonids in streams. American Fisheries Society 	Special Publication 19:83-138.

Chastain, J. et. al. 2002. The Fishes of Rickreall Creek.

Curry K.D. and Spacie A. 1984. Differential use of stream	habitat by spawning catostomatids.  American Midland	Naturalist 111:267-279.

Duncan, Jason. Active member of the Polk County Sportsmen’s 	Club. Phone Communication. November 10, 2003.

Eaton, J.G., Scheller R.M. 1996. Effects of climate on fish 	thermal habitat in streams of the United States, 	Limnology and Oceanography, 1109-1115.

Ellis, J.G. 1974. The Jumping Ability and Behavior of Green

Sunfish (Lepomis cyanellus) at the Outflow of a 1.6-ha Pond. Transaction of the American Fisheries Society. No.3, Vol.103

Emig, J. W. 1966. Largemouth bass, pp. 332-353; smallmouth		bass, pp. 354-365; redear sunfish, pp. 392-398; brown		bullhead, pp. 463-475. In A. Calhoun, ed., Inland			Fisheries Management. California Fish and Game.

Hart, J.L., Pacific Fishes of Canada. Fisheries Research

Board of Canada, John Deyell Company, 1980. pp,21-129

Kahler, T.H., and T.P. Quinn, Juvenile and Resident 	salmonid movement and passage through culverts, 	Fisheries Research Institute, University of 	Washington. Seattle WA.1998.

Kolok, A.S., Morphological and physiological correlates 	with swimming performance in juvenile largemouth bass, 	American Physiological Society, 1992.

Maezono,Y. and T. Miyashita, Community-level impacts

induced by introduced largemouth bass and bluegill in farm ponds in Japan. Biological Conservation. Vol. 109, no.1. 2003.

Marchetti, M. Ecological Effects of Non-native Fish Species

in Low Elevation Streams of the Central Valley, California. Dissertation Abstracts International Part B: Science and Engineering. Vol.60, no.4, 1999.

Mattson K. and Gallegher A. 2001. Rickreall Watershed

Assessment. Ecosystems Northwest, Mt. Shasta, CA.

Miller, K. D. and R. J. Kramer. 1971. Spawning and early		life history of largemouth bass (Micropterus				salmoides) in Lake Powell, pp. 73-83, in G. E. Hall		ed., Reservoir fisheries and limnology. Am. Fish.		Soc. Spec. Publ. No. 8.

Morgan, G. D. 1951. The life history of the bluegill			sunfish, Lepomis macrochirus, of Buckeye Lake (Ohio),		J. Sci. Lab. Denison Univ. 42(4):21-59, plus plates.

Moyle, P. B. 1976. Inland fishes of California. University		of California Press, Berkeley. 405 pp

Computer programs and websites:

Fish Xing, San Dimas Technology and Development Center, 2001.

ODFW Fish Passage Program

http://www.dfw.state.or.us/ODFWhtml/InfoCntrFish/Management/FishPassage.ham

Accessed 17 September 2003

USGS 14190700 Rickreall Creek Near Dallas, OR. National		Water Information System, U.S. Geological Survey.			Gauge data from 01 Oct. 1957 to 30 Sept. 1978

http://www.waterdata.usgs.gov/nwis/help?codes_help#dv_cd.

Accessed 20 May 2003

USGS 11102, Temperature Records from Rickreall Creek at		State Farm Road, LASAR#:  11102,,,,,. Temperature Unit		S/N: 459183,,,,,2001.  U.S. Geological Survey, from 15		May 2001 to 23 Oct. 2001.

Wood, B.M., and M.B. Bain. 1005. Morphology and 	microhabitat use in stream fish. Canadian Journal of 	Fisheries and Aquatic Science 52:1487-1498.

8.2 Bibliography

# Aadland, L.P. 1993. Stream habitat types: Their fish 	assemblages and relationship to Flow. North American 	Journal of Fisheries Management 13:790-806.

Adams, S.R., Hoover, J.J., Killgore, K.J. Swimming 	Performance of the Topeka Shiner(Notropis topeka) an 	endangered Midwestern Minnow, The American Midland 	Naturalist: Vol 144, No. 1, pp. 178-186.

Avila, V.L. 1976. A field study of nesting behavior of male 	bluegill sunfish (Lepomis Macrochirus rafinesque). 	American Midland Naturalist 96:195-206.

Bastasch, Rick. 1998. Waters of Oregon. Corvallis: Oregon

State University Press.

Beitinger, T.L., and J.J. Magnuson. 1975. Influence of 	social rank and size on thermoselection behavior of 	bluegill (Lepomis macrochirus). Journal of Fisheries 	Research Board of Canada 32:2133-2136.

Beitinger, T.L., and J.J. Magnuson. 1976. Low thermal 	responsiveness in the bluegill,(Lepomis macrochirus). 	Journal of Fisheries Research Board of Canada

33:293-295.

Bell, M. Fisheries Handbook of Engineering Requirements and		Biological Criteria, Portland, Oregon: US Army Corps		of Engineers, North Pacific Division, 1990.pp 1~1-	35~7.

Berry, C.R., and Pimentel, R. Swimming Performance of Three 	Rare Colorado River Fishes, Transactions of the 	American Fisheries Society 114:397-402, 1985.

Bjornn, T.C. and D.W. Reiser. 1991. Habitat requirements of 	salmonids in streams. American Fisheries Society 	Special Publication 19:83-138.

Cherry, D.S., K.L. Dickerson, J. Cairns, Jr., and J.R. 	/Stauffer. 1997. Preferred, avoided,and lethal 	temperatures of fish during rising temperature 	conditions. Journal of Fisheries Research Board of 	Canada 34:239-246.

Cherry, D.S., K.L. Dickerson and J. Cairns, Jr. 1975. 	Temperatures selected and avoided by fish at various 	acclimation temperatures. Journal of Fisheries 	Research Board of Canada 32:485-491.

Committee on Stream Restoration and Species Recovery, House 	Bill 3002, Pertains to Fish passage regulations and 	barrier restrictions. 71st Oregon Legislative Assembly-	2001 regular session.

Coutant, C.C. 1977.  Compilation of temperature preference 	data. Journal of Fisheries Research Board of Canada 	34:739-745.

Hickman, G.D., and M.R. Dewey. 1973. Notes on the upper 	lethal temperature of the Dusky stripe shiner 	(Notropis pilsbryi),and the bluegill(Lepomis 	macrochirus). Transactions of the American Fisheries 	Society 102:838-840.

Jones, C.R., Kicenuik, J.W., and Bamford, O.S. 1974, 	Evaluation of the Swimming Performance of Several Fish 	Species from the Mackenzie River. J. Fish. Res.Board 	Can.31:1641647.

Kane and Behlke D.L. Kane, PO Box 755860. Fairbanks, AK

99775-5860, Personal communication in WSTC Report.

Mirati A.H., Assessment of road Culverts for Fish Passage 	Problems On State and county owned Roads, Statewide 	summary report. Sept. 1999.

Robinson G.E., Mirati A., Allen M. Oregon Road/Stream 	Crossing Restoration Guide, Advance Fish Passage 	Training Version. (June 8, 1999)

Schaffer, J.F., W.I.L Utterschmidt, and L.G. Hill. 1999. 	Physiological performance and stream microhabitat use 	by the centrarchids (Lepomis megalotis) and (Lepomis 	macrochirus). Environmental Biology of Fishes 54:303-	312).

Spence, B.C, et all 1996. An ecosystem approach to salmonid 	conservation. TR-4501-96-6057. ManTech Environmental 	Research Service Corp., Corvallis, OR.

Stuber, R.J., G. Gebhart, and O.E. Maughan. 1982. Habitat 	suitability index models: Bluegill. United States 	Department of Interion FWS/OBS-82/10.8.

Wang, J.C.S., Fishes of the Sacramento-San Joaquin Estuary		and Adjacent Waters, California: A Guide to the Early		Life Histories, Technical Report 9 (FS/B10-4ATR 86-9),		1986.

Websites:

http://www.dfw.state.or.us/ODFWhtml/InfoCntrFish/Management/stream_Road.htm

Salmonid distribution for the Willamette River Basin.

http://www.oregonstate.edu/dept/nrimp/information/fishdistdata.htm.

Accessed 23 April 2003

9.0 Illustrations

9.1 Field sketch of Villwok’s Ford

9.2 Photographs

- Appendix

10.1 Culvert analysis graphs

Fig. 1:  Comparison of discharge (cfs) to water depth (ft) for adult coho salmon (Oncorhyncus kisutch), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow conditions.

Fig 2:  Comparison of discharge (cfs) to leap velocity (ft/s) for adult suckers (catostomatid spp.).  The vertical lines indicate low (2 cfs) and high (40 cfs) discharges.  The red section of the curve indicates water velocity is greater than sucker jumping ability.

Fig 3:  Comparison of stream discharge (cfs) to velocity (ft/s) in culvert for adult steelhead (Oncorhyncus mykiss).  The vertical blue lines indicate low and high passage flow for culvert.  The blue area on the curve indicates passable velocity.  The red area of curve indicates excessive velocity.

Fig. 4:  Comparison of discharge (cfs) to water depth (ft) for adult Chinook salmon (Oncorhyncus tschawytscha), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow conditions.

Fig. 5:  Comparison of discharge (cfs) to water depth (ft) for juvenile Chinook salmon (Oncorhyncus tschawytscha), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow conditions.

Fig. 6:  Comparison of discharge (cfs) to water depth (ft) for juvenile coho salmon (Oncorhyncus kisutch), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow.

Fig. 7:  Comparison of discharge (cfs) to water depth (ft) for adult cutthroat trout (Salmo clarkii), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow.

Fig. 8:  Comparison of discharge (cfs) to water depth (ft) for juvenile cutthroat trout (Salmo clarkii), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow.

Fig. 9:  Comparison of discharge (cfs) to water depth (ft) for adult longear sunfish (Lepomis megalotis), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow.

Fig. 10:  Comparison of discharge (cfs) to water depth (ft) for adult sucker (Catastomus catastomus), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow.

Fig. 11:  Comparison of discharge (cfs) to water depth (ft) for adult steelhead(Onchorhynchus mykiss), from 2 to 40 cfs.  The red part of the curve, at left, indicates insufficient depth to allow passage at that discharge.  The blue part of the curve indicates passable water depth.  The vertical lines are low (2 cfs) and high (40 cfs) flow.

Fig 12:  Comparison of stream discharge (cfs) to velocity (ft/s) in culvert for adult chinook (Oncorhyncus tschawytscha).  The vertical blue lines indicate low and high passage flow for culvert.  The blue area on the curve indicates passable velocity.  The red area of curve indicates excessive velocity.

Fig 13:  Comparison of discharge (cfs) to leap velocity (ft/s) for juvenile salmonids.  The vertical lines indicate low (2 cfs) and high (40 cfs) discharges.  The red section of the curve indicates water velocity is greater than sucker jumping ability.

Fig 14:  Comparison of discharge (cfs) to leap velocity (ft/s) for adult cutthroat (Salmo clarkii).  The vertical lines indicate low (2 cfs) and high (40 cfs) discharges.  The red section of the curve indicates water velocity is greater than sucker jumping ability.

Fig 15:  Comparison of discharge (cfs) to leap velocity (ft/s) for adult sucker (Catastomus catastomus).  The vertical lines indicate low (2 cfs) and high (40 cfs) discharges.  The red section of the curve indicates water velocity is greater than sucker jumping ability.

Fig 16:  Comparison of discharge (cfs) to leap velocity (ft/s) for adult longear sunfish (Lepomis megalotis).  The vertical lines indicate low (2 cfs) and high (40 cfs) discharges.  The red section of the curve indicates water velocity is greater than sucker jumping ability.

Fig 17:  Comparison of stream discharge (cfs) to velocity (ft/s) in culvert for adult steelhead (Oncorhyncus mykiss).  The vertical blue lines indicate low and high passage flow for culvert.  The blue area on the curve indicates passable velocity.  The red area of curve indicates excessive velocity.

Fig 18:  Comparison of discharge (cfs) to leap velocity (ft/s) for adult rainbow trout (Oncorhyncus mykiss).  The vertical lines indicate low (2 cfs) and high (40 cfs) discharges.  The red section of the curve indicates water velocity is greater than sucker jumping ability.

Fig 19:  Comparison of stream discharge (cfs) to velocity (ft/s) in culvert for adult coho (Oncorhyncus kisutch).  The vertical blue lines indicate low and high passage flow for culvert.  The blue area on the curve indicates passable velocity.  The red area of curve indicates excessive velocity.

Fig 20:  Comparison of stream discharge (cfs) to velocity (ft/s) in culvert for adult cutthroat (Salmo clarkii).  The vertical blue lines indicate low and high passage flow for culvert.  The blue area on the curve indicates passable velocity.  The red area of curve indicates excessive velocity.

# Text boxes

High flows at Villwok’s Ford, Rickreall creek (Polk County, Oregon; 11 April 2003).

Low flows at Villwok’s Ford, Rickreall Creek (Polk County, Oregon; 18 August 2003).

Villwok’s Ford as a spillway, looking upstream of Rickreall Creek (Polk County, Oregon; 1 March 2003).

Villwok’s Frod as a culvert, looking upstream of Rickreall Creek (Polk County, Oregon; 12 July 2003).

Current fish box (as of 12 July 2003)  Villwok’s Ford (Polk County, Oregon)

Fish box at Villwok’s Ford during high water flows when the ford acts as a spillway (Polk County, Oregon)

Culvert at Villwok’s Ford during low flows (Polk County, Oregon; 12 July 2003).